Комплектация:
    GSM / GPRS / GPS- плата × 1шт
    GSM антенна × 1шт
    Внешняя антенна GPS (В ) × 1шт
    Спикер × 1шт
    Крепежные винты × 2шт
    9В адаптер питания × 1шт
    Кабель USB Type A папа, порт коммутатора мини -B мужской порт × 1шт

GSM/GPRS/GPS Shield is an Arduino shield based on the Quad-band GSM/GPRS/GPS module SIM908.

### Features

General

- Arduino connectivity, connects to Arduino Board directly

- NOKIA speaker & mic, supports hands-free phone talk

- Onboard CP2102 for easily debugging through USB interfere

- Onboard 74HC125, for time-shared controlling GSM and GPS port through single serial port

- Earphone insert detection & call vibration

- Quad-band 850/900/1800/1900MHz

- GPRS multi-slot class 10

- GPRS mobile station class B

- Compliant to GSM phase 2/2+

  - Class 4 (2 W @ 850/900 MHz)

  - Class 1 (1 W @ 1800/1900 MHz)

- Control via AT commands (GSM 07.07, 07.05 and SIMCom enhanced AT Commands)

- SIM application toolkit

- Supply voltage range :

  - GPRS: 3.2 ~ 4.8 V

  - GPS: 3.0 ~ 4.5V

- Operation temperature : -40 °C to +85 °C

SMS

- Point-to-point MO and MT

- SMS cell broadcast

- Text and PDU mode

Audio

- Tricodec

  - Half rate (HR)

  - Full rate (FR)

  - Enhanced Full rate (EFR)

- Hands-free operation

- Echo cancellation

GPRS

- GPRS class 8/10: max. 85.6 kbps (downlink)

- PBCCH support

- Coding schemes CS 1, 2, 3, 4

- PPP-stack

CSD

- CSD up to 14.4 kbps

- USSD

- Non transparent mode

GPS

- Receiver type

  - 42-channel

  - GPS L1 C/A code

  - High-performance STE engine

- Sensitivity

  - Tracking: -160 dBm

  - Cold starts : -143 dBm

- Time-To-First-Fix

  - Cold starts : 30s (typ.)

  - Hot starts : 1s (typ.)

- Accuracy

  - Horizontal position : <2.5m CEP

- Power consumption (GSM engine in idle mode)

  - Acquisition : 77mA

  - Tracking : 76mA

- Earphone jack : SIM908 2nd analog voice channel output

- GSM antenna connector : SMA interface

- Arduino expansion connector : for connecting with an Arduino board

- GSM antenna connector

- SIM908 control interface

- GPS antenna connector

- USB TO UART interface

- NOKIA original speaker : SIM908 1st analog voice channel output

- Arduino reset button

- SIM908

- SIM908 network indicator : blinking slowly when network registration is successful

- Power indicator

- Mic : SIM908 1st analog voice channel input

- SIM card slot

- CP2102

- UART Tx/Rx indicator

- Power switch

- 6V~9V DC power jack

- Vibration motor

- 74HC125

- NCP2890 power amplifier : amplifies the SIM908 1st analog voice channel

- MIC29302 power chip

- SIM908 analog output positive jumper :

  - open it when NCP2890 is enabled

  - short it when NCP2890 is disabled

- SIM908 analog output negative jumper :

  - open it when NCP2890 is enabled

  - short it when NCP2890 is disabled

- NCP2890 enable jumper :

  - short the EN and VBAT to enable

  - short the EN and GND to disable